## Slide 1: Objective
Modeling and simulation of physical and MAC layers of IEEE WLANs
Standards considered: 802.11n & 802.11ac at 2.4 GHz and 5 GHz

## Slide 2: Outline
Scenarios and performance metrics
Throughput results: 802.11n and 802.11ac
Methodology and details
Plan for 2021

## Slide 3: Performance Metrics and Modeling Scenarios
Performance metrics
  Throughput
  Latency
  Packet error rate
  Range
Models with simulation parameters
  Scenario 1: Aircraft stationary at different distances from an access point
    Focus on standardized channel models for which verification is possible
  Scenario 2: Aircraft in motion towards gate with single access point
  Scenario 3: Aircraft in motion in taxi way covering multiple access points

## Slide 4: Throughput vs. Distance Plots
802.11n:
802.11ac:
EIRP (dBm) | Noise Figure (dB) | BW (MHz) | No. of spatial streams
18 vs. 20 | 11 | 20 | 2
18 | 11 vs. 16 | 40 | 1
18 | 11 | 20 vs. 40 | 3
EIRP (dBm) | Noise Figure (dB) | BW (MHz) | No. of spatial streams
18 | 11 | 20 vs. 40 vs. 80 vs. 160 | 4, 2

## Slide 5
Throughput Results for IEEE 802.11n
  EIRP: 18 & 20 dBm
  Noise figures: 11, 13.5, 16 dB
  Bandwidth: 20 & 40 MHz for 11n, and 20, 40, 80 & 160 MHz for 11ac
  1x1, 2x2, 3x3 & 4x4 antenna configurations
  Spatial streams: 1, 2, 3 & 4

## Slide 6: Effect of EIRP [BW 20 MHz, 2 Spatial Streams]
EIRP (dBm) | 18 vs. 20
Noise figure (dB) | 11
BW (MHz) | 20
No. of spatial streams | 2
As EIRP increases, range increases

## Slide 7: Effect of Noise Figure [BW 40 MHz, 1 Spatial Stream]
EIRP (dBm) | 18
Noise figure (dB) | 11 vs. 16
BW (MHz) | 40
No. of spatial streams | 1
As noise figure increases, range decreases

## Slide 8: Effect of Bandwidth [3 Spatial Streams]
EIRP (dBm) | 18
Noise figure (dB) | 11
BW (MHz) | 20 vs. 40
No. of spatial streams | 3
As channel bandwidth increases, throughput increases & range decreases

## Slide 9
Throughput Results for IEEE 802.11ac

## Slide 10: Effect of Bandwidth [MCS 0, 4 spatial streams]
EIRP (dBm) | 20
Noise Figure (dB) | 11
BW (MHz) | 20 vs. 40 vs. 80 vs. 160
No. of spatial streams | 4
As channel bandwidth increases, throughput increases & range decreases
MCS 0

## Slide 11: Effect of Bandwidth [MCS 2, 2 spatial streams]
EIRP (dBm) | 20
Noise Figure (dB) | 11
BW (MHz) | 20 vs. 40 vs. 80 vs. 160
No. of spatial streams | 2
As channel bandwidth increases, throughput increases & range decreases
MCS 2

## Slide 12
Methodology

## Slide 13: Technical Details: Four Step Approach
Step 1: Obtain PER vs. SNR plots for different MCSs
  Validate the simulation results by comparing it with results in standard documents
Step 2: Obtain PER vs. distance plots for different EIRPs and noise floors
Step 3: Develop rate adaptation algorithm and benchmark
Step 4: Extend to Scenarios 2 and 3
EIRP
SNR
Noise Floor
Channel Model
Distance
PER
MCS
Throughput
PER vs. distance
For different EIRP
For different Noise Floor
Throughput vs. distance
For different EIRP
For different Noise Floor

## Slide 14: Plots Generated and Verification Approach
PER and throughput for different SNRs obtained for all MCSs
  For 802.11n and 802.11ac
  Channel Models B, C, and D
PER vs. SNR curves validated with those in “Next Generation Wireless LANs,” E. Perahia and R. Stacey, Cambridge Univ. Press

## Slide 15: Changing Channel Model
Can control breakpoint distance (dBP)
  Results shown were for dBP = 50 m
Need to figure out how to change power delay profile

## Slide 16: Transmit Receive Chain Simulation for an MCS
Every packet
Each module corresponds to a function in MATLAB
Receiver
Packet Detect
Frequency correction
Time sync
Demodulation
Channel estimation
Data Decoding
PSDU
MCS
SNR
PER
Bit comparison
Channel
Channel model
AWGN
Transmitter
Packet Waveform Generation
PSDU

## Slide 17: Throughput Calculation
Given a distance, EIRP, noise floor, the SNR is calculated
PER is obtained using the data generated for different MCS
Throughput is calculated using the rate and PER
EIRP
Distance Pathloss
SNR
Noise Floor
PER
MCS
Throughput
Rate

## Slide 18: Plots Coming Up
Validation plots: PER vs. SNR for 802.11n, Model D
Outstanding issue

## Slide 19: Validation: PER vs. SNR: Model D, 802.11n
SNR (dB) at which PER is 10%:
  Reference: 10, 11, 12, 13, 32, 35, 37, 38
  Simulation: 10, 10, 11, 11, 32, 36, 37, 39

## Slide 20: Outstanding Issue: Error Floor
PER exhibits error floors for higher MCSs in Models E & F in both 11n & 11ac
Occurs only for highly dispersive channel models
PER vs. SNR; Model-E; 802.11n

## Slide 21
Rate Adaptation Algorithms

## Slide 22: Rate Adaptation Algorithms
Goal: Choose rate, number of spatial streams and bandwidth
Several algorithms available in literature
  Minstrel: Default in Linux.
  MiRA (MIMO – Aware Rate Adaptation)
  RAMAS (Rate Adaptation for Multi-Antenna Systems)
  Damysus
  Few algorithms require modifications or special signalling

## Slide 23: Minstrel: A Closer Look
Initial rate selection
Organize rates in groups
  MCS 0 to 9 - 1 spatial stream 20 MHz; MCS 0 to 9 - 1 spatial stream 40 MHz; ...
  Same for 2, 3 & 4 spatial streams
Remove/trim groups not supported by the AP
Optional: From each group, pick rates compatible with initial signal budget
Compute the transmission time for each selected rate
Transmit at the rate with the smallest transmission time

## Slide 24: Picking Good Rates that Change with Conditions
At regular intervals (e.g., 100 ms), enter a sampling period
During a sampling period, pick a random rate in a group
Try the rate, within the max retry limit for this group (e.g., 3)
If the rate results in a higher throughput than the previous rate, rank the rate up
Repeat until the end of the sampling period
Retain 3 rates:
  Highest throughput
  Second highest throughput
  Highest probability (least loss/retries)

## Slide 25: Retry Chain: When Transmission Fails
For each rate, a max retry count is defined
  Count is affected by the historical throughput for that rate
  Retry time is assigned (percentage of maximum of 79.2 ms)
  Number of retries depends on the data rate
  Retry more of those rates that have been highly successful in the past
Retry chain logic
79.2 ms
low
throughput
high
Retry time calculation:

## Slide 26: Summary
Throughput vs. distance plots obtained for models B, C, D, E & F
  Based on PER vs. SNR data obtained for all models
MATLAB issue: Error floors for highly dispersive channel models (E and F)
Rate adaptation algorithms survey initiated
  Minstrel: Default benchmark