## Slide 1: AIOT data management - Overview
Anomaly Class | Description
0 | NO anomaly
1 | Ventilation efficiency
2 | Independent source
3 | Fuming event
4 | Event after anomaly
Severity | Indicator
0 | Low
1 | Medium
2 | High
Storage Space
Adaptive Storage
Data generation model
CO2 across zones
TPH
Passenger Count
Anomaly class
Severity
Adaptive decision block and severity predictor

## Slide 2: Data generation model
Notes: Cabin ECS system using Simulink
Flight conditions, passenger count, diffusion model written using MATLAB
Cabin divided into 6 zones

## Slide 3: Example - Class 2 anomaly in zone 2 for 50% occupancy
Chart: CO2 (ppm) vs Time(s)
Anomaly:
Independent source of CO2 in Zone 2

## Slide 4: Anomaly & severity level prediction
Input Features
Adaptive Decision Block
Anomaly Class
Anomaly Class | Description
0 | NO anomaly
1 | Ventilation efficiency
2 | Independent source
3 | Fuming event
4 | Event after anomaly
Input Features:
CO2 across zones [1:6]
Rate of change of CO2 [1:6]
Humidity
Passenger Count
(total features: 14)
Severity Level
Predictor
Severity level | Description
0 | Low severity
1 | Intermediate Severity
2 | High Severity

## Slide 5: Adaptive decision block
Humidity > Humidity_th
Max deviation between zones > dev_th
Avg_slope < Slope_th
CO2(i) < CO2_th
Class 4
Class 2
Class 1
Class 3
Class 0
Generation Model
Linear Regression based predictors
Decision elements
Anomaly Class
CO2 threshold
Humidity threshold
Threshold for maximum
deviation between zones
Passenger count
CO2 [1,6] ,Humidity
Yes
Yes
Yes
Yes
No
No
No
No
ADAPTIVE DECISION BLOCK
i is the Zone Number
CO2(i) : CO2(1),…, CO2(6),
Anomaly Class | Description
0 | NO anomaly
1 | Ventilation efficiency
2 | Independent source
3 | Fuming event
4 | Event after anomaly
Notes: A transparent method of anomaly detection was desired for the controller
Few Algorithms like linear classifiers, logistic regression, decision trees were tried, but the anomaly predictions were noisy.
An adaptive decision block was designed. It can accurately predict the anomalies.
  Linear regression was used to predict thresholds for making decision block
  Anomaly detection done by the decision block

## Slide 6: Anomaly and severity predictions using Decision Block
Class 1
Class 2
Class 3
time
CO2 (ppm)
Class (0-4)
Severity (0-2)
time
time
Notes: The plots demonstrate that our Decision Block can accurately predict the anomalies and their severity

## Slide 7: Adaptive Storage using Linear Interpolation
Chart: CO2 (ppm) vs Time(s)
Class 0
Class 2
Severity 1
Class 2
Severity 0
Class 0
Class 4
Severity 1
Class 4
Severity 0
Notes: Time series data divided into windows based on anomaly class and severity

## Slide 8: Adaptive Storage using Linear Interpolation
Play
Notes: In a given window of time series data, we start interpolating linearly between moving data points.
If the interpolated values fall below an error threshold, we continue the process
If the threshold is breached, we store the latest point

## Slide 9: Designing a Cost Function
Cost = (1-A).(Normalized Error threshold)+(A).(Normalized Storage Space)
Severity 0
Severity 1
Severity 2
Cost Function:
Notes: There is an inverse relationship between error threshold and storage space consumed
Larger errors allow us to consume less space but reduce reconstruction accuracy
An optimum error threshold needs to be chosen depending upon available storage space and severity of data.
This optimization is done using cost functions over windows (batches) of time series data

## Slide 10: Data management implementation in TICK stack
Data Generation Model
Influx DB (Temporary Database)
Kapacitor (batch process) Adaptive Storage Algorithm
Influx DB (Final Database)
Query data for defined window size
Points to be stored
Chronograf (Reconstruction and visualization)
CO2 across zones
TPH
Passenger Count

## Slide 11: TICK stack results
Generated Data
10800 Data Points
Adaptive Storage
282 Data Points Stored
Final file size with InfluxDB’s compression
2367 bytes
File size in InfluxDB before compression
4819 bytes
Generated Data
10800 Data Points
Final file size with InfluxDB’s compression
70488 bytes
File size in InfluxDB before compression
166,290 bytes
Reduction in Storage Space = 96.64%
Examples in the following slides…

## Slide 12: Generated data at zones 1 & 3
Time
CO2 (ppm)
Data Generation Model
Influx DB (Temporary Database)
CO2 across zones
TPH
Passenger count
Kapacitor (batch process) Adaptive Storage Algorithm
Influx DB (Final Database)
Query data for defined window size
Points to be stored
Chronograf (Reconstruction and visualization)
Zone 3 (anomalous)
Zone 1

## Slide 13: Adaptively stored data at zone 3 (anomalous)
Data Generation Model
Influx DB (Temporary Database)
CO2 across zones
TPH
Passenger count
Kapacitor (batch process) Adaptive Storage Algorithm
Influx DB (Final Database)
Query data for defined window size
Points to be stored
Chronograf (Reconstruction and visualization)
Time
CO2 (ppm)

## Slide 14: Reconstructed data
Data Generation Model
Influx DB (Temporary Database)
CO2 across zones
TPH
Passenger count
Kapacitor (batch process) Adaptive Storage Algorithm
Influx DB (Final Database)
Query data for defined window size
Points to be stored
Chronograf (Reconstruction and visualization)
Time
CO2 (ppm)

## Slide 15: Adaptively stored data at zone 1 (Non-anomalous)
Data Generation Model
Influx DB (Temporary Database)
CO2 across zones
TPH
Passenger count
Kapacitor (batch process) Adaptive Storage Algorithm
Influx DB (Final Database)
Query data for defined window size
Points to be stored
Chronograf (Reconstruction and visualization)
Time
CO2 (ppm)

## Slide 16: Reconstructed data
Data Generation Model
Influx DB (Temporary Database)
CO2 across zones
TPH
Passenger count
Kapacitor (batch process) Adaptive Storage Algorithm
Influx DB (Final Database)
Query data for defined window size
Points to be stored
Chronograf (Reconstruction and visualization)
Time
CO2 (ppm)